## Slide 1: VOLUMETRIC VIDEO // PLENOPTIC LIGHTFIELD // MULTI CAMERA METHODOLOGIES
JORDAN HALSEY // VR PLAYHOUSE

## Slide 2
VOLUMETRIC VIDEO // PLENOPTIC LIGHTFIELD // MULTI CAMERA METHODOLOGIES
Pro: Highly realistic seated viewing experience Large lighting datasets
Reflections and refractions behave as n the real world
 |  |  | Con: | Extremely large datasets
 |  |  |  | Playback is view dependent
 |  |  |  | Cgi integration and post effects need to be rendered with exact camera matching
 |  |  |  | Rendering, rendering, rendering...
 |  |  |  | Complicated file structure
 |  |  |  | Necessity for highly controlled lighting

## Slide 3
VOLUMETRIC VIDEO // PLENOPTIC LIGHTFIELD // POST PRODUCTION METHODOLOGIES

## Slide 4
VOLUMETRIC VIDEO // PLENOPTIC LIGHTFIELD // POST PRODUCTION METHODOLOGIES

## Slide 5
VOLUMETRIC VIDEO // PLENOPTIC LIGHTFIELD // POST PRODUCTION METHODOLOGIES
Lightfield, as we know it will never be other than a view dependent solution Combining Lightfield for volumetric reconstruction
Specular/Reflection information based off per camera calculations View Dependent

## Slide 6
GEOMETRY RE-CONSTRUCTION // LIDAR DATA // PHOTOGRAMMETRY
Geometry reconstruction techniques Filling in missing or incomplete data Photogrammetry for object re-construction

## Slide 7
GOOGLE JUMP PROGRAM // VOLUMETRIC RECONSTRUCTION // POST PRODUCTION METHODOLOGIES
Pro:
Automatic stitching through the cloud
Stitched media delivered as 8K top/bottom stereo Stereo depth maps
CGI can be integrated easily in a variety of ways Can be turned into a room scale experience Can be integrated into the game engine
Any CGI post effects can be rendered easily without the need for elaborate camera set-ups Playback is not view dependent
Con:
Lighting is baked ( More on this later....) Can create large data sets
Currently data is 8 bit
Depth information needs refining through post production

## Slide 8
GOOGLE JUMP PROGRAM // VOLUMETRIC RECONSTRUCTION // POST PRODUCTION METHODOLOGIES
Top/Bottom stereo Nadir fixes
Depth clean up

## Slide 9
GOOGLE JUMP PROGRAM // VOLUMETRIC RECONSTRUCTION // POST PRODUCTION METHODOLOGIES
Volumetric reconstruction pre-processed and post-processed.

## Slide 10
GOOGLE JUMP PROGRAM // VOLUMETRIC RECONSTRUCTION // POST PRODUCTION METHODOLOGIES
Over corrected right eye depth map
A sphere integrated with the volumetric video

## Slide 11
GOOGLE JUMP PROGRAM // VOLUMETRIC RECONSTRUCTION // POST PRODUCTION METHODOLOGIES
Distance based scale correction
Can be embedded as an attribute on the data for playback

## Slide 12
INTEGRATED CGI // DEEP BASED COMPOSITING
Deep based compositing techniques for cgi integration
Spatial rectification between the lat-long world and the cgi world Matching z-depth for correct stereo between cgi and shot lat long

## Slide 13
GOOGLE JUMP PROGRAM // VOLUMETRIC RECONSTRUCTION // POST PRODUCTION METHODOLOGIES
Deep re-construction in for CGI Integration

## Slide 14
OBJECT EXTRACTION AND ISOLATION THROUGH DEPTH SLICING
Automatic z through depth data Altering depth of field
Re-lighting effects through normals

## Slide 15
GEOMETRY RE-CONSTRUCTION THROUGH POINT CLOUD MESHING AND TEXTURE RE-PROJECTION
Using the data for geometry isolation Using the data for geometry creation Texture projection

## Slide 16
GOOGLE JUMP PROGRAM // VOLUMETRIC RECONSTRUCTION // POST PRODUCTION METHODOLOGIES
CGI Integration with Stereo footage from the Google Jump program

## Slide 17
GOOGLE JUMP PROGRAM // VOLUMETRIC RECONSTRUCTION // POST PRODUCTION METHODOLOGIES
Object isolation for integration with CGI

## Slide 18
GOOGLE JUMP PROGRAM // VOLUMETRIC RECONSTRUCTION // POST PRODUCTION METHODOLOGIES
Fluid interaction with collisions

## Slide 19
GOOGLE JUMP PROGRAM // VOLUMETRIC RECONSTRUCTION // DE-LIGHTING
Using the provided environment we are able to sample the diffuse lighting contribution With the provided lighting contribution we can project a ray on the data

## Slide 20
DEEP RENDERING // VOLUMETRIC RECONSTRUCTION // POST PRODUCTION METHODOLOGIES
Using deep renders for volumetric reconstruction Deep represents multiple float values per pixel

## Slide 21
DEEP RENDERING // VOLUMETRIC RECONSTRUCTION // POST PRODUCTION METHODOLOGIES

## Slide 22
DEEP RENDERING // VOLUMETRIC RECONSTRUCTION // POST PRODUCTION METHODOLOGIES